## Slide 1: Filtering in Frequency Domain

## Slide 2
Why does a lower resolution image still make sense to us? What do we lose?
Image: http://www.flickr.com/photos/igorms/136916757/
Sampling

## Slide 3: Sampling
Upsampling
Downsampling

## Slide 4
Throw away every other row and column to create a 1/2 size image
Subsampling by a factor of 2

## Slide 5
A ‘bar’ in the big images is a hair on the zebra’s nose; in smaller images, a stripe; in the smallest, the animal’s nose
Figure from David Forsyth
Image pyramid

## Slide 6: Algorithm for downsampling by factor of 2
Start with image of w x h
Sample every other pixel
  im_small = image[ ::2:, ::2 ]
Repeat until im_small is 1 pixel large.
Hays

## Slide 7: Image sub-sampling
Throw away every other row and column to create a 1/2 size image.
1/4
1/8
Steve Seitz

## Slide 8: Subsampling without filtering
1/4 (2x subsample)
1/8 (4x subsample)
1/2
Steve Seitz

## Slide 9: Sampling and aliasing

## Slide 10: Aliasing problem
Aliasing is a signal processing term.
Aliasing occurs when you sample a signal too slowly (at a frequency comparable to or smaller than the signal being measured).
As a result, an incorrect frequency and/or amplitude is obtained.

## Slide 11: Aliasing problem
1D example (sinewave):
Source: S. Marschner

## Slide 12: Aliasing problem
Source: S. Marschner
1D example (sinewave):

## Slide 13: Aliasing problem
Sub-sampling may be dangerous….
Characteristic errors may appear:
  “car wheels rolling the wrong way in movies”
  “checkerboards disintegrate in graphics”
  “striped shirts look funny on color television”
    Moiré patterns
Source: D. Forsyth; Wikipedia

## Slide 14: Aliasing in video
Slide by Steve Seitz

## Slide 15: Videos
[YouTube; JoinBuzzirk; phrancque]
Notes: https://www.youtube.com/watch?v=Y1yHMy0-4TM
https://www.youtube.com/watch?v=jQDjJRYmeWg

## Slide 16: Aliasing in graphics
Source: A. Efros

## Slide 17: Nyquist-Shannon Sampling Theorem
When sampling a signal at discrete intervals, the sampling frequency must be  2  fmax
fmax = max frequency of the input signal
This allows us to reconstruct the original perfectly from the sampled version
good
bad
v
v
v

## Slide 18: How to fix aliasing?
Solutions?

## Slide 19: Better sensors
Solutions:
Sample more often

## Slide 20: Anti-aliasing
Solutions:
Sample more often
Get rid of all frequencies that are greater than half the new sampling frequency
  Will lose information
  But it’s better than aliasing
  Apply a smoothing (low pass) filter
Hays

## Slide 21: Anti-aliasing
Forsyth and Ponce 2002

## Slide 22: Algorithm for downsampling by factor of 2
Start with image(h, w)
Apply low-pass filter
  im_blur = imfilter( image, fspecial(‘gaussian’, 7, 1) )
Sample every other pixel
  im_small = im_blur( 1:2:end, 1:2:end );
Hays

## Slide 23: Subsampling without filtering
1/4 (2x subsample)
1/8 (4x subsample)
1/2
Steve Seitz

## Slide 24: Subsampling with Gaussian pre-filtering
G 1/4
G 1/8
Gaussian 1/2
Steve Seitz
Gaussian Pyramid [Burt and Adelson, 1983]